## Slide 1: BIM-based semantic enrichment for environmental analyses using semantic textual similarity
Dr.-Ing. Kasimir Forth, 22.05.2025

## Slide 2: Research overview
BIM
LLM/ STS
New buildings
PhD
BIM4EarlyLCA
MP
BEPS
LCA

## Slide 3: Problem: semantic enrichment of BIM
Wall name:
Exterior_CMU_Insulated
Materials:
Concrete
Rigid insulation
Room:
Cleaning room
Building Information Model
Building Energy Model
Storage:
Lighting
Electric equipment
Infiltration
Ventilation
Setpoint (Heating/ cooling)
Layer 1:
Reinforcement steel (2%)
Concrete C20/25 (98%)
Layer 2:
Mineral wool (facade insulation)
Layer 3 (missing in BIM):
Interior lime plaster
Layer 4 (missing in BIM):
Application primer emulsion, dispersion paint
Life Cycle Assessment
Insulated exterior mass wall:
Layer 1: Stucco
Layer 2: Concrete
Layer 3: Typical Insulation
Layer 4: Gypsum
Wall set
MEP space type
LCA
datasets

## Slide 4: Semantic Textual Similarity (STS)
NLP model | Similarity measure
- | Levenshtein distance
Lexical-Semantic Nets | Synset similarity, e.g. Shortest path
Transformer-based Large Language Models (LLM) | Cosine similarity

## Slide 5: Rise of LLMs
ranked by capabilities, sized by billion parameters used for training

## Slide 6: Transformers
(Vaswani et al., 2017)
Attention is all you need (Vaswani et al., 2017)
Encoder-Decoder Structure, but with attention replacing RNN
Recurrent layers are not needed anymore
Attention mechanisms to process sequences in parallel, rather than sequentially
Transformers require a large amount of computational power, especially for longer sequences
https://medium.com/@vimal.parakhiya/decoding-large-language-models-a-deep-dive-into-the-self-attention-mechanism-967d6207d4ae

## Slide 7: Semantic Textual Similarity (STS)
Deep Learning
Transfer Learning: instead of training a model from scratch, use models pre-trained on a large dataset  fine-tuning with small dataset of specific task (reuse general-puprose LLM, avoid over-fit)
Natural Language Processing (NLP): convert text to numbers (vectors for distance, direction)
Semantic Textual Similarity (STS): contextual similarity by cosine similarity measure
Word Embeddings: Word2Vec, BERT
Sentence Embeddings: Universal Sentence Embeddings

## Slide 8: Semantic Textual Similarity (STS)
Language Model
Similarity measure
Cosine similarity
Transformer-based Large Language Models (LLM)
model = SentenceTransformer('bert-base-uncased‘)
Example:
cosine(concrete, cement) = 94,72 %
cosine(concrete, brick) = 83,33 %
[ 7.93417156e-01 8.29650760e-02 -5.23231030e-02 -2.17395127e-01
-8.32237974e-02 -4.45498765e-01 -1.26688731e+00 1.06830096e+00
-1.28666349e-02 -4.68899488e-01 -2.02071592e-01 -1.12816297e-01
2.69040763e-02 -4.06338722e-02 -6.89153850e-01 3.63473892e-01
1.11588106e-01 3.40398014e-01 4.84653145e-01 -2.50174493e-01
-3.53295594e-01 1.23900771e-01 1.11937448e-01 -6.00896478e-02
-3.12148392e-01 5.75537622e-01 9.36730027e-01 -5.60345173e-01
5.78632295e-01 -2.32372671e-01 1.69208661e-01 4.12962675e-01
8.03140178e-02 7.45790243e-01 1.17071569e+00 5.55167198e-02
5.11050224e-01 1.16298109e-01 9.20241475e-02 -9.87720788e-02
8.48577380e-01 5.31948626e-01 9.33959424e-01 -1.32031858e-01
9.00211811e-01 -5.83819568e-01 8.29421043e-01 -3.51497233e-02
1.84658214e-01 1.58213913e-01 -8.74938011e-01 2.04985574e-01
2.12046504e-01 2.44288906e-01 4.61633772e-01 4.49981354e-02
2.33117819e-01 2.25253910e-01 -5.51613033e-01 2.82539278e-01
2.29331344e-01 -2.41953611e-01 -1.69738233e-01 -9.45715532e-02
-3.71751010e-01 8.33538234e-01 1.52621496e+00 -4.84886497e-01
-6.13606155e-01 -5.57552934e-01 2.55793810e-01 -6.92006886e-01
-4.54984093e+00 -9.26977396e-02 -9.40760851e-01 3.21871191e-02
-2.16004774e-01 9.72391486e-01 1.59482658e-01 5.63296318e-01
2.68730372e-02 7.18028486e-01 6.60112977e-01 3.96659315e-01
3.07498455e-01 8.34056139e-01 -9.23457742e-01 -2.11890787e-01
-2.71091163e-01 -3.53735745e-01 -6.20788261e-02 1.69884533e-01
-1.26969349e+00 -1.24605739e+00 1.20583892e+00 2.81507641e-01
5.37502527e-01 2.25627422e-02 -3.65057230e-01 -3.24838996e-01
-6.73068821e-01 -5.55100083e-01 1.07220717e-01 7.51177743e-02
1.66999847e-01 -5.65669760e-02 -5.37174821e-01 1.97182149e-01
-4.85657305e-01 -1.11633591e-01 2.20505241e-02 5.47537506e-01
2.90986821e-02 -2.91154683e-02 2.24938482e-01 -2.10108027e-01
3.73894393e-01 -7.86128998e-01 9.21761215e-01 1.62584692e-01
-1.37326717e-01 -5.73756874e-01 4.02603030e-01 -5.42482495e-01
6.53179139e-02 -2.96782076e-01 2.84805834e-01 7.83194184e-01
3.37617815e-01 -5.08406579e-01 5.62487006e-01 -4.30884808e-01
-1.25970215e-01 -3.65098596e-01 3.71568829e-01 4.17400122e-01
9.65109020e-02 -3.05784672e-01 2.10360259e-01 -1.59321725e-01
-2.36658186e-01 7.30582327e-03 -7.98410177e-02 8.79049838e-01
7.04189360e-01 6.05629325e-01 1.38470769e+00 -5.37037373e-01
-1.99557826e-01 6.51216283e-02 -6.25732541e-03 -5.78052342e-01
1.10243547e+00 2.29339153e-01 3.28719079e-01 -7.76662678e-02
-8.21682155e-01 -8.00741017e-02 -3.72380257e-01 2.23960578e-01
-4.26753163e-01 3.52671117e-01 1.93373784e-01 9.66680884e-01
-7.24408865e-01 -4.63018149e-01 -2.46008560e-01 -3.53394419e-01
-5.13954759e-01 1.58451557e-01 -7.71883726e-02 1.94275439e-01
-4.01165813e-01 -1.64506599e-01 3.39347392e-01 2.44310722e-01
3.79376084e-01 1.13751984e+00 1.40489742e-01 5.84856093e-01
-8.58848333e-01 -1.00996271e-02 3.53537858e-01 -9.77599502e-01
2.69020647e-01 3.32219511e-01 -6.85725510e-01 6.66895270e-01
-1.93581432e-01 -6.22250140e-03 7.48491883e-01 -6.89815581e-01
-7.87970424e-02 1.10012487e-01 -2.43320256e-01 -2.24682540e-02
-3.57071310e-02 -1.59448966e-01 5.26317358e-02 5.60355783e-01
8.92967582e-01 -1.61882773e-01 3.23787928e-01 -8.11748505e-02
-8.88107419e-02 -3.04983258e-01 8.74929354e-02 -1.05804515e+00
-2.95586050e-01 1.79473773e-01 5.42225957e-01 -6.63240433e-01
-3.77704948e-01 2.11305737e-01 3.03511024e-02 -3.40882301e-01
3.09231400e-01 8.73124719e-01 -2.78483182e-01 5.67523777e-01
-3.14469934e-01 -4.36114132e-01 -7.01730609e-01 -1.66682661e-01
-5.00753522e-01 -2.59878486e-01 -1.92758143e-02 -7.27440953e-01
-7.90189326e-01 3.34672332e-01 -3.10532808e-01 -4.10227001e-01
5.83508611e-01 1.43373716e+00 3.59099001e-01 5.18511117e-01
6.08694255e-01 -2.08158582e-01 7.45840013e-01 -1.58267528e-01
-4.90233451e-02 7.38504082e-02 5.05458534e-01 3.18468213e-01
7.10750073e-02 -4.66306508e-01 1.73503920e-01 5.65444469e-01
6.80207834e-02 3.12143624e-01 4.08284962e-02 -8.66480947e-01
4.83854711e-02 6.64438546e-01 -8.11929703e-02 -5.08115888e-01
4.66900468e-01 -3.58327448e-01 -9.11293775e-02 9.12261844e-01
-2.84069419e-01 -4.12509561e-01 -1.32767960e-01 7.05837160e-02
1.27318501e+00 -6.35570958e-02 -6.71987891e-01 5.19288778e-01
-3.96836579e-01 -2.83882141e-01 4.42507923e-01 9.11628380e-02
2.36631855e-02 -4.12411541e-01 -3.50247234e-01 6.25860691e-01
3.07056010e-02 1.00811219e+00 1.89153284e-01 4.58502144e-01
1.49567771e+00 -2.83000290e-01 -2.02027470e-01 5.46329260e-01
-1.27066851e-01 -3.11615288e-01 -6.11885190e-01 1.58946753e-01
3.57714370e-02 -3.01720500e-02 -4.15183067e-01 5.18441856e-01
-4.93103266e-01 5.47533706e-02 -4.99157667e-01 3.92679155e-01
-1.75812587e-01 -2.51360625e-01 -4.88607734e-02 3.43798280e-01
-1.34233758e-01 9.96006012e-01 -2.61857539e-01 7.27524757e-02
2.37225801e-01 -5.57635352e-02 -4.84738648e-01 -6.53715208e-02
-1.95787162e-01 4.16614771e-01 -1.98015228e-01 -1.57584861e-01
8.04035902e-01 -6.38814092e-01 8.33452865e-02 4.46270019e-01
3.97350967e-01 1.92115307e-01 9.43569243e-01 -9.21103477e-01
-6.03356600e-01 -4.32370842e-01 4.32011306e-01 -1.72371641e-01
6.53024673e-01 -3.05769652e-01 -4.81042981e-01 2.63146944e-02
3.85118186e-01 4.83796000e-01 -5.16638994e-01 -3.21957201e-01
-5.80514848e-01 1.19222388e-01 -1.10021257e+00 -3.26117605e-01
1.71316528e+00 5.62162735e-02 9.50355828e-03 6.64872944e-01
-5.39093077e-01 2.66112536e-01 1.79609895e-01 4.05989766e-01
-3.71596873e-01 -6.48266673e-01 -2.76225656e-02 3.37252110e-01
1.84154809e-02 4.36090529e-01 1.10443246e+00 1.36103049e-01
-9.86590028e-01 -1.37833089e-01 5.37889838e-01 -1.99922055e-01
-5.76203823e-01 3.32201868e-01 3.40699732e-01 -8.47409308e-01
-4.21136558e-01 -6.15115583e-01 2.01261625e-01 -3.87923419e-01
5.21669686e-01 -5.55739880e-01 -3.18780154e-01 -6.02304675e-02
-2.84414947e-01 -2.51529336e-01 -3.07689309e-01 4.87605631e-01
7.72765428e-02 3.99792373e-01 2.59738833e-01 1.45707622e-01
1.89506114e-01 2.95574725e-01 -1.22231627e+00 5.52306652e-01
-1.12291574e+00 6.41016960e-01 6.72316551e-02 -4.66993451e-02
1.90138876e-01 -9.00714278e-01 8.36803019e-03 -1.69438422e-02
-5.92977822e-01 -6.50723338e-01 -5.18072784e-01 1.56105012e-01
-3.59951437e-01 3.87876928e-02 -8.72222066e-01 -3.30499373e-03
8.93233716e-01 -1.20444655e-01 1.41373527e+00 -3.20495158e-01
7.75437474e-01 3.06213588e-01 -3.02815020e-01 -5.42093292e-02
1.22276336e-01 -6.05847120e-01 2.34447181e-01 3.80676538e-02
3.63660723e-01 2.21035540e-01 -7.63507128e-01 -9.39299107e-01
5.88006198e-01 -3.65265012e-01 1.60602391e-01 -3.06411594e-01
-6.28080249e-01 7.12894261e-01 -5.28892338e-01 -9.97515917e-01
8.36685374e-02 -4.27438676e-01 -6.54080749e-01 5.63178062e-01
-2.52053589e-02 -6.11614466e-01 -5.46239853e-01 -3.43902320e-01
-4.79859889e-01 -4.56492364e-01 -7.58665726e-02 6.47508204e-01
-1.06110370e+00 -2.09942795e-02 -7.83309102e-01 -2.37874240e-02
-3.91762376e-01 -5.91796756e-01 -3.93111929e-02 -3.35438877e-01
1.40335038e-02 -4.24379915e-01 6.47341013e-02 8.78049508e-02
1.37439162e-01 -1.96740180e-01 -7.84101486e-01 -4.66014415e-01
5.06868064e-02 2.47897916e-02 -4.98707086e-01 3.76915455e-01
1.24918312e-01 -1.69203132e-01 4.12189662e-01 -8.61794233e-01
-6.78871155e-01 -1.11508757e-01 -6.78885579e-01 2.59941131e-01
-1.46831349e-02 -2.56075114e-02 3.66047621e-01 -8.52454782e-01
2.12828606e-01 -7.41954446e-01 -1.23513341e-01 -7.37691343e-01
6.09610200e-01 -8.40500236e-01 4.47567165e-01 -4.35227931e-01
4.99380231e-01 7.13433385e-01 -6.05246425e-01 -1.13739826e-01
4.65037405e-01 1.89203620e-01 5.82755953e-02 4.61967811e-02
-3.23371917e-01 -1.92195207e-01 1.97781801e-01 -3.69411409e-01
-1.06980197e-01 2.59817421e-01 8.00486058e-02 9.51058418e-03
3.02866101e-01 1.88881904e-03 1.15565985e-01 -1.40413582e-01
8.92238140e-01 -1.18600452e+00 5.56488872e-01 7.37461686e-01
9.39744592e-01 3.86909008e-01 1.57811141e+00 3.81787807e-01
-2.15259790e-01 -7.78924108e-01 1.16847619e-01 -1.19649720e+00
-8.46069038e-01 -5.40075421e-01 -7.51968145e-01 1.23884773e+00
-4.84374344e-01 -6.97239697e-01 -4.12126154e-01 -1.16760693e-01
-3.24822247e-01 1.90009072e-01 -3.34495574e-01 2.92782366e-01
4.63660121e-01 5.77235341e-01 -1.68476567e-01 8.80004644e-01
3.10535312e-01 -1.05125956e-01 1.21627942e-01 4.72453117e-01
1.39813340e+00 5.55745602e-01 3.66614878e-01 3.77451122e-01
-3.90589476e-01 -4.43344414e-01 -6.02789998e-01 7.83340216e-01
8.27827305e-02 1.44587800e-01 2.04348385e-01 -2.54174918e-01
2.80319154e-01 8.53757441e-01 -6.89254403e-02 -2.49775499e-01
-9.49245930e-01 2.89742827e-01 5.22765100e-01 2.25976050e-01
-9.63110328e-01 -4.47067112e-01 -4.46701676e-01 -1.42508850e-01
-1.29194602e-01 -1.12778580e+00 -2.39949301e-01 2.50462331e-02
-7.76521623e-01 1.81496888e-02 7.68089175e-01 -3.12704369e-02
-4.93964851e-01 9.01968718e-01 -2.61514187e-01 6.01293892e-03
-2.94394314e-01 -6.03471816e-01 -5.70318997e-01 -4.58910167e-02
-5.05368710e-01 9.27282274e-01 1.05101094e-02 -3.04134578e-01
-1.41699597e-01 5.59040785e-01 1.53377652e-03 -3.78428251e-02
-4.17304873e-01 4.28673744e-01 -2.60846496e-01 -4.54545438e-01
-4.14908350e-01 4.70070571e-01 -5.01714945e-01 2.51757562e-01
-1.88131362e-01 -2.60722250e-01 -1.85079545e-01 -2.83006579e-01
3.55063051e-01 1.88687950e-01 -8.42502594e-01 -6.71386957e-01
1.24344110e+00 -2.46767998e-02 -6.47865593e-01 1.01868495e-01
-1.48657620e-01 6.63356408e-02 7.70462975e-02 -2.96890616e-01
-6.68320179e-01 3.53565782e-01 5.94213083e-02 -7.08389342e-01
3.07263434e-01 4.04187113e-01 1.10012245e+00 -7.99584091e-02
-9.39760685e-01 4.89687771e-01 -5.42291999e-01 -7.43937433e-01
1.57381043e-01 3.34519073e-02 -3.97372961e-01 -8.70960429e-02
-1.20021963e+00 -9.80041862e-01 -3.47414285e-01 -6.70193434e-01
1.38850540e-01 6.26738787e-01 4.29225773e-01 5.00610650e-01
-2.91431785e-01 1.08529115e+00 4.86341119e-01 -2.52187014e-01
-3.61164868e-01 5.63975692e-01 1.41157135e-01 -5.64380735e-02
8.57155442e-01 -4.35316533e-01 7.73539543e-02 -3.33524793e-02
8.60679150e-02 5.15364647e-01 3.54378492e-01 1.09625168e+01
4.19652104e-01 1.19410813e+00 -8.43115568e-01 -1.81533322e-01
4.92928088e-01 -1.42919272e-01 1.52804360e-01 -4.36707288e-01
-2.41291970e-02 -3.60829234e-01 -4.16250885e-01 6.52575612e-01
-8.27805340e-01 -8.27721059e-01 -2.69816041e-01 -5.15553713e-01
3.88892502e-01 -3.03525746e-01 5.23445964e-01 -6.59306645e-01
-5.03555417e-01 4.56714451e-01 3.88177127e-01 5.02301991e-01
1.01066113e+00 -5.39673530e-02 -2.26399422e-01 -4.51337963e-01
-2.81162769e-01 -1.15852880e+00 -3.74303401e-01 1.13456559e+00
-6.05286777e-01 2.11646184e-01 -3.95028025e-01 3.94750237e-01
2.98588276e-01 -1.04184580e+00 4.94031578e-01 -1.53053850e-01
-3.74180079e-01 1.00309312e+00 8.22239935e-01 -2.31395155e-01
5.29232621e-01 -3.96025091e-01 1.35788068e-01 -1.15176804e-01
3.20620686e-02 -6.45730555e-01 -5.29725969e-01 5.13912916e-01
-5.16817510e-01 -5.84204316e-01 -3.03734615e-02 -7.02928722e-01
-7.01311648e-01 -2.59553432e-01 3.74039024e-01 1.82371736e-01
5.33550903e-02 -7.89539933e-01 -1.93450242e-01 3.00196499e-01
-9.13644195e-01 8.05464506e-01 8.33888412e-01 6.43017292e-01
-1.76989049e-01 -3.66481453e-01 -4.23485458e-01 -5.85697770e-01
4.27237213e-01 3.03330213e-01 -2.25601673e-01 -1.41714349e-01
3.20419848e-01 -3.73093754e-01 2.70743966e-01 -4.29871142e-01
-1.92693651e-01 -3.91600192e-01 -6.85277104e-01 -1.01155281e+00
-1.54100060e-02 1.55142963e-01 -1.38860986e-01 -4.33848023e-01
3.54915053e-01 5.12295485e-01 1.02278478e-01 9.56505477e-01
6.49094462e-01 7.99110711e-01 3.65924001e-01 7.89373875e-01
3.48500758e-01 -6.93622351e-01 -6.47317886e-01 5.44491589e-01
1.88926220e-01 3.92342985e-01 -4.26074505e-01 -8.83782983e-01
4.26133156e-01 3.77885550e-01 7.76099443e-01 -1.82269767e-01
-1.06373107e+00 3.57803315e-01 8.71052384e-01 -7.35188782e-01
-1.76440746e-01 5.35256207e-01 -6.52544260e-01 3.21372926e-01
8.19673091e-02 4.44514379e-02 -1.04063594e+00 2.81850398e-01
1.18795180e+00 3.33518744e-01 -2.34514147e-01 2.65670180e-01
3.22413921e-01 -2.02874511e-01 -1.20547223e+00 1.38298035e+00
3.21854532e-01 -5.60756803e-01 -1.48127985e+00 -1.08538294e+00]]
Vector embeddings of BERT with 768 dimensions
Devlin, J., Chang, M.-W., Lee, K., & Toutanova, K. (2018). BERT: Pre-training of Deep Bidirectional Transformers for Language Understanding. https://arxiv.org/pdf/1810.04805

## Slide 9: Semantic matching using LLM/ STS
Example IfcElement – Exterior walls
Legend:
Nodes:
Workflows:
STS
IFC Model
Database
Similar. anal. & matching
Tokenization: splitting the text into discrete units, i.e., singular words
Vectorization: converting the textual terms/ tokens into a vector representation/ embeddings
Similarity calculation
Tokeniz.
Vectoriz.
Vectoriz.
Similarity of tokens
Vectoriz.
Similarity of terms
Save maximum similarities
2
Selection & enrichment
3
Select & enrich of data with highest cosine similarity to item
Filtering
IfcProduct
Classification
Filter
Data from external DB
1
Vectoriz.
Tokeniz.
General
Comparison
Iteration
CMU_Insulated
Reinforced concrete wall
CMU
Reinforced
concrete
wall
51.55%
61.49%
66.68%
66.53%
66.68%

## Slide 10: LCA knowledge database
Forth, K.; Abualdenien, J.; Borrmann, A. (2023): Calculation of embodied GHG emissions in early building design stages using BIM and NLP-based semantic model healing. Energy and Buildings 284

## Slide 11: LCA result range of window variants
Forth, K.; Abualdenien, J.; Borrmann, A. (2023): Calculation of embodied GHG emissions in early building design stages using BIM and NLP-based semantic model healing. Energy and Buildings 284
Chart: GWP of window variants
| Aluminiumrahmen, 2-Scheiben verglast | Aluminiumrahmen, 3-Scheiben verglast | Holzrahmen, 2-Scheiben verglast | Holzrahmen, 3-Scheiben verglast
 | 906.38 | 1263.71 | 614.38 | 1150.37
Chart: GWP range of window variants
Minimum | 614.38
Quantil 25% | 219
Quantil 25% | 194.995
Quantil 75% | 150.33
Maximum | 85.005
Mean | 983.71

## Slide 12: LLM-based semantic matching for LCA
Element matching performance:
Chart: 
| a) correctly matched | b) no correct matching element available in LKdb | c) wrong element classification | d) no valid element classification | e) too little information/ details | f) wrong matched
Case study 1 | 0.79763 | 0.010427 | 0.10237 | 0.0014218 | 0.048341 | 0.03981
Case study 2 | 0.73616 | 0 | 0 | 0.25733 | 0 | 0.0065147
Case study 3 | 0.67979 | 0.11678 | 0.013032 | 0.011313 | 0.16039 | 0.018688
Case study 4 | 0.88368 | 0.00069989 | 0.10232 | 0.00027996 | 0.012598 | 0.00041993
Case study 5 | 0.89402 | 0 | 0.083305 | 0.00017176 | 0.017004 | 0.0054964
Real-world case studies
Forth, K.; Abualdenien, J.; Borrmann, A. (2023): Calculation of embodied GHG emissions in early building design stages using BIM and NLP-based semantic model healing. Energy and Buildings 284

## Slide 13: LLM-based semantic matching for LCA
LCA result ranges (GWP):
2.
2
Forth, K.; Abualdenien, J.; Borrmann, A. (2023): Calculation of embodied GHG emissions in early building design stages using BIM and NLP-based semantic model healing. Energy and Buildings 284

## Slide 14: LLM-based semantic matching for MP
Adding domain-specific abbreviations
  BIM abbreviations
  AEC abbreviations
  Combination of AEC- & BIM abbreviations
Applying different loss functions for fine-tuning , such as
  CosineSimilarityLoss: positive (0.8), negative (0.3)
  Contrastive Loss: positive (1), negative (0)
  Multiple Negative Ranking Loss (MNRL)
Adding different/ multiple labels for further context information (Element name, classification, IfcType, etc.) using Softmax Loss Function
Adding negative/ contradicting word pairs
Filtering word pairs according to IfcTypeObject
5:
CMU concrete masonry unit
Masonry Brick 1/ 0.8
Masonry Brick 1
EW_CMU_Insul Brick 2
331 Brick 3
IfcWall Brick 4
Masonry Concrete 0/ 0.3
2.
4.
1.
3.
IfcWall, IfcSlab, IfcWindow…
MEP Mech., Engin., Plumb.
IfcMaterial Match. Mat. Label
Strategies for fine-tuning & improving matching performance
Forth, K.; Berggold, P.; Borrmann, A. (2024): Domain-specific fine-tuning of LLM for material matching of BIM elements and Material Passports. i3CE 2024, Carnegie Mellon University, Pittsburgh, USA, 2024

## Slide 15: LLM-based semantic matching for MP
Forth, K.; Berggold, P.; Borrmann, A. (2024): Domain-specific fine-tuning of LLM for material matching of BIM elements and Material Passports. i3CE 2024, Carnegie Mellon University, Pittsburgh, USA, 2024
Chart: Overview of error clusters
| base model | C3
Correct Matches | 44 | 80
Error clust. 1: Reinf. Concrete | 31 | 15
Error clust. 2: Insulation | 8 | 3
Error clust. 3: Aluminium | 5 | 0
Error clust. 4: Steel | 5 | 0
Error clust. 5: others | 7 | 2
Chart: Matching accuracy of combined strategies
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
base model | 0.44262 | 0.45902 | 0.45902 | 0.4918 | 0.52459 | 0.55738 | 0.57377 | 0.57377 | 0.59016 | 0.60656
C1: S1c + S2c + S5 | 0.4918 | 0.57377 | 0.59016 | 0.63934 | 0.63934 | 0.67213 | 0.68852 | 0.70492 | 0.72131 | 0.7377
C2: S1c + S2c + S3 + S5 | 0.44262 | 0.5082 | 0.54098 | 0.55738 | 0.57377 | 0.60656 | 0.65574 | 0.65574 | 0.68852 | 0.70492
C3: S1c + S4b + S5 | 0.52459 | 0.65574 | 0.72131 | 0.72131 | 0.7377 | 0.7541 | 0.7541 | 0.77049 | 0.80328 | 0.80328

## Slide 16: LLM-based semantic matching for MP
Confusion matrix of the best performing LLM
Error cluster 1: Reinforced concrete
Error cluster 3&4: Metal
Error cluster 2: Insulation
Error cluster 5: Others
Forth, K.; Berggold, P.; Borrmann, A. (2024): Domain-specific fine-tuning of LLM for material matching of BIM elements and Material Passports. i3CE 2024, Carnegie Mellon University, Pittsburgh, USA, 2024

## Slide 17: LLM-based semantic matching for BEPS
Strategies for fine-tuning & improving matching performance
Monolingual fine-tuning:
Applying different loss functions for monolingual fine-tuning, such as
  Cosine Loss
  Contrastive Loss
  MultipleNegativesRrankingLoss (MNRL)
Adding negative/ contradicting word pairs (already included in MNRL)
Adding abbreviations including
  general ones in the AEC industry and
  about construction and material nomenclature usually given in German BIM practice
Adding context, such as IfcTypes, isExternal, classifications using Softmax Loss Function and multiple labels
Multilingual fine-tuning:
using different multilingual student LLM, such as
  LaBSE
  XLM-RoBERTa and
  Distilluse-v2
Adding more multilingual pairs of domain-specific materials translations
1.
3.
II:
2.
4.
I:
Forth, K.; Borrmann, A. (2024): Semantic enrichment for BIM-based Building Energy Performance Simulations using Semantic Textual Similarity and fine-tuning multilingual LLM. Journal of Building Engineering 95

## Slide 18: LLM-based semantic matching for BEPS
Forth, K.; Borrmann, A. (2024): Semantic enrichment for BIM-based Building Energy Performance Simulations using Semantic Textual Similarity and fine-tuning multilingual LLM. Journal of Building Engineering 95
Room-specific matching of program types:
Element-specific matching of construction sets:

## Slide 19: BIM4EarlyLCA: design decision support
LCA visualization strategies
BIM-based 3D color code
Heat map
Bar charts diagrams
Uncertainty visualization strategies
Transparency of 3D elements
Gradient color ranges
Boxplot diagrams
Element 1
Element 2
Element n
Element 1
Element 2
Element n
Chart: 
| x | y | z
 | 8 | 10 | 6
Forth, K.; Hollberg, A.; Borrmann, A. (2023): BIM4EarlyLCA: An interactive visualization approach for early design support based on uncertain LCA results using open BIM. Developments in the Built Environment 16

## Slide 20: BIM4EarlyLCA: design decision support
Forth, K.; Hollberg, A.; Borrmann, A. (2023): BIM4EarlyLCA: An interactive visualization approach for early design support based on uncertain LCA results using open BIM. Developments in the Built Environment 16

## Slide 21: Conclusion PhD
Automation
Database structure
LLM fine-tuning
BEPS
Decision assistance
Semi-automated
Fully automated
No fine-tuning
Monolingual fine-tuning
Multilingual fine-tuning
Unstructured
(EPEA)
Pre-structured
(NREL)
Detailed structured
(LKdb)
MP
LCA

## Slide 22: Outlook – workshop focus
Comparing different LLM-based workflows for matching the LCA material dataset to IfcMaterials
  Activity III
  STS-based
  matching approach
  Activity IV
  Prompt-based
  matching approach
Using text embeddings as raw vectors
Calculates cosine similarity
Static
Using instructional input to the LLM
Context-aware reasoning
Dynamic

## Slide 23: Outlook – workshop
1. Category level
2. Category level
3. Category level
Material dataset level

## Slide 24: Thank you!
Circular Engineering for Architecture
cea